PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the Pole Vault Landing Pad Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - Pole Vault Landing Pad Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		POLE VAULT LANDING PAD SYSTEMS

- Pole Vault Landing Pad System- Shall be as manufactured by AAE:

  - Model # SPV-30XL, Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 30” high x 21’-6” wide x 24’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, two (2) front units each 30” – 18” x 6’-6” x 8’-3” and two (2) front units each 18” x 4’  6” x 9’-7” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes two (2) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SWC-30XL, Weather Cover, one (1) Weather Cover 22oz. double knife-coated vinyl (standard color gray, custom colors available), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment to be used w/ Model # SPV-30XL

  - Model # SPV-32XL, Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 32” high x 21’-6” wide x 24’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units comprised of a four (4) layer cross pattern foam assembly, two (2) front units each 30” – 18” x 6’-6” x 8’-3” and two (2) front units each 18” x 4’  6” x 9’-7” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover with 2” top pad to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ additional 2” thick solid foam pad and skirted 18oz. double knife-coated vinyl sides (color as specified) top pad includes heavy duty zipper surround for foam insertion, box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes two (2) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SWC-32XL, Weather Cover, one (1) Weather Cover 22oz. double knife-coated vinyl (standard color gray, custom colors available), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment to be used w/ Model # SPV-32XL

  - Model # SPV-32XXL, Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 32” high by 21’-6” wide by 27’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes nine (9) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, two (2) front units each 30” – 18” x 6’-6” x 8’-3”, two (2) front units each 18” x 4’  6” x 9’-7” and two (2) front units each 18” x 3’ x 8’-10” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover with 2” top pad to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes two (2) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SWC-32XXL, Weather Cover, one (1) Weather Cover 22oz. double knife-coated vinyl (standard color gray, custom colors available), box-tacked heavy duty nylon web strap w/ military-spec snap hooks for easy attachment to be used w/ Model # SPV-32XXL

  - Model # SPV-30XL-DF, Double Front Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 30” high x 21’-6” wide x 35’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, four (4) front units each 30” – 18” x 6’-6” x 8’-3” and four (4) front units each 18” x 4’  6” x 9’-7” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes four (4) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SPV-32XL-DF, Double Front Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 32” high x 21’-6” wide x 35’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, four (4) front units each 30” – 18” x 6’-6” x 8’-3” and four (4) front units each 18” x 4’  6” x 9’-7” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover with 2” top pad to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes four (4) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SPV-30XXL-DF, Double Front Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 30” high x 21’-6” wide x 41’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, four (4) front units each 30” – 18” x 6’-6” x 8’-3” and four (4) front units each 18” x 4’  6” x 9’-7” and two (2) front units each 18” x 3’ x 8’-10” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes four (4) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

  - Model # SPV-32XXL-DF, Double Front Landing pad meets and exceeds all NFHS, NCAA and IAAF rules and specifications, overall assembled system measures 32” high x 21’-6” wide x 41’-0” deep, base units include foam types 18120 (18# - 1.1 density), 33120 (33# - 1.2 density) and 40130 (40# - 1.3 density) complies w/ ASTM F1162 - 02 Standard Specification for Pole Vault Landing Systems; system includes seven (7) Base Units: three (3) rear base units, each 30” x 7’-2” x 13’, comprised of a four (4) layer cross pattern foam assembly, four (4) front units each 30” – 18” x 6’-6” x 8’-3” and four (4) front units each 18” x 4’  6” x 9’-7” and two (2) front units each 18” x 3’ x 8’-10” are all solid foam construction;  system includes Base Unit Encasements in heavy duty vinyl: 18oz. double knife-coated vinyl sides (color gray), 22oz. double knife-coated vinyl bottom (color black), vinyl-coated mesh top w/ double welded and quad stitched seams (color gray), each unit includes heavy duty zipper surround for foam insertion, box-tacked heavy duty nylon web buckling system w/ military-spec Velcro, box-tacked heavy duty nylon handles, military-spec o-rings w/ box-tacked heavy duty nylon web strap;  system includes one (1) Skirted Breather Cover to encase entire system w/ vinyl-coated mesh top double welded and quad stitched seams (color as specified) w/ skirted 18oz. double knife-coated vinyl sides (color as specified), box-tacked strap w/ military-spec snap hooks for easy attachment;  system includes four (4) Side Pads model # PVB-32XL, sloped solid foam units encased in 18oz. double knife-coated vinyl (color as specified), box-tacked buckling system w/ military-spec Velcro, pads surround pole vault standards;  system includes one (1) Vault Box Collar model # VBC-S, 4” thick solid foam collar encased in 18oz. double knife-coated vinyl (color yellow), two (2) sewn on vinyl flaps w/ male Velcro, box-tacked strap w/ military-spec snap hooks for easy attachment to front base units, two (2) strips of female style Velcro w/ adhesive back to attach to vault box; PLEASE NOTE: Warning Labels on all units

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All concrete footings for athletic equipment shall be installed as indicated on the drawings and in accordance with Section 03300, Cast-in-Place Concrete.

- All sleeves required for athletic equipment installation shall be set plumb and true to line and grade in concrete as indicated on the drawings and per manufacturer's recommendation.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -