PART 1	GENERAL

1.1	SUMMARY

- Provide all equipment and materials, and do all work necessary to furnish and install the Field Hockey Equipment, as indicated on the drawings and as specified herein.

1.2	RELATED WORK

- Examine Contract Documents for requirements that affect work of this section.  Other specification sections that directly relate to work of this Section include, but are not limited to:

  - Section 02200 - Earthwork; Excavation and Backfill and establishment of subgrade elevations.

  - Section 02511 - Asphalt Concrete Pavement

  - Section 02535 - Synthetic Track Surfacing

  - Section 02542 - Synthetic Field Surfacing

  - Section 03300 - Cast-in-Place Concrete; Concrete foundations and bases for goals.

1.3		REFERENCES

- Comply with applicable requirements of the following standards.  Where these standards conflict with other specified requirements, the most restrictive requirements shall govern.

      - U.S. Tennis Court and Track Builders Association

      - National Federation of State High School Associations (NFSHSA)

      - National Collegiate Athletic Association (NCAA)

      - International Amateur Athletic Foundation (I.A.A.F.)

      - Manufacturers Data and Recommended Installation Requirements.

1.4		SUBMITTALS

- Manufacturers Product Data

            - Provide manufacturer’s product literature, technical specifications and other data prior to actual field installation work for Architect or Owner’s Representative review.

# Shop Drawings

  - Provide drawings of manufacturers recommended installation and foundation requirements prior to actual field installation work for Architect or Owner’s Representative review.

1.5		QUALITY ASSURANCE

- Manufacturers warranties shall pass to the Owner and certification made that the product materials meet all applicable grade trademarks or conform to industry standards and inspection requirements.

1.6	DELIVERY, STORAGE AND HANDLING

- Materials delivered to the site shall be examined for concealed damage or defects in shipping. Any defects shall be noted and reported to the Owner’s Representative.

- Replacements, if necessary, shall be immediately re-ordered, so as to minimize any conflict with the construction schedule.

- Sound materials shall be stored above the ground under protective cover or indoors so as to provide proper protection.

PART 2	PRODUCTS

2.1		MANUFACTURERS

- Manufacturers and product selections named are provided to establish the minimum standard.

      - Field Hockey Equipment - As manufactured by AAE (Aluminum Athletic Equipment Co.); 1000 Enterprise Drive, Royersford, PA 19468; Toll Free (800) 523-5471.

2.2		Field Hockey EQUIPMENT

- Field Hockey Goals - Shall be as manufactured by AAE:

  - Model # FHG (standard portable), Goal Face 2" square x 1/8"wall aluminum tube with 1/8" rounded corners welded "U" one-piece frame 7'2" x 12'4", Rear Frame 2" square x 1/8" welded box frame 7'2" x 12'4", Lower Brace 1-1/4" x 2.30" x 1/8"wall rectangular tube with 1/8” rounded corners welded to ¼" thick aluminum plate framed 18" x 44", Upper Brace 2" square x 1/8"wall aluminum tube with 1/8” rounded corners x 43-1/2" aluminum tube w/ ¼" thick aluminum offset flanges on each end, Back Bottom Boards made of 3/8" thick black UV stabilized HDPE, 18" x 48", Side Bottom Boards made of 3/8" thick black UV stabilized HDPE, 18" x 46", Molded Net Clips made of black UV stabilized nylon, Wheels (four) 10" Semi-Pneumatic Wheels w/ 3/4" round 304 stainless steel axles & cotter hairpin, all stainless steel hardware with nylon-loc nuts for minimal maintenance

  - Model # FHG-FIH (portable international FIH), Goal Face 2" (50mm) square x 1/8"wall aluminum tube with 1/8" rounded corners welded "U" one-piece frame 7'2" x 12'4", Rear Frame 2" square x 1/8" welded box frame 7'2" x 12'4"  (3.66 metres by 2.14 metres inside to inside) with 3/8" diameter welded aluminum weave for net attachment, Side Brace 2" (50mm) square x 1/8" wall aluminum tube with 1/8" rounded corners welded to ¼" thick aluminum plate with 3/8" diameter welded aluminum weave framed with rear gusset supports to , Back Bottom Boards made of three (3) each 3/8" thick black UV stabilized HDPE, 18" x 48" (460mm x 3.66 metres long), Side Bottom Boards made of two (2) each 3/8" thick black UV stabilized HDPE, 18" x 46" (460mm x 1.20 metres long), 1/8" thick UV stabilized polyethylene twine for net attachment to aluminum weave, Wheels (four) 10" Semi-Pneumatic Wheels w/ 3/4" round 304 stainless steel axles & cotter hairpin, all stainless steel hardware with nylon-loc nuts for minimal maintenance

  - Model # FIH-SB (Indoor Field Hockey Side Board), 3-1/8” wide bottom x 3-7/8” wide top x 3-7/8” height with a side pitch angle of 5.71° x 12’0” in length, 6061T6 aluminum extrusion with interlocking channel slots and bounce back control rib, two stainless steel locking pins and two 1” diameter rubber grommet finger holes, meets all FIH Rule requirements

  - Model # FHN-1 (standard field hockey goal net) 2.5 mm twine polyethylene braided 1-1/2" square mesh net, UV stabilized Black, measures 12' wide by 7' high by 48" depth with a 1/4" MFP rope border

  - Model # FHN-FIH (international field hockey goal net) 4 mm twine high tenacity poly propylene knotless 45mm square mesh net, UV stabilized Green, measures 3.66 metres wide by 1.80 metres high by 0.90 metres top depth and 1.20 metres bottom depth with a 8mm MFP rope border

PART 3	EXECUTION

3.1  		INSPECTION

- Examine the areas and conditions where equipment and systems are to be installed and notify the contractor of conditions detrimental to the proper and timely installation and completion of the work.

- Do not proceed with the work until unsatisfactory conditions have been corrected by the contractor in a manner acceptable and to the satisfaction of the Architect/Engineer or Owner's Representative.

3.2	INSTALLATION

- All athletic equipment shall be installed as indicated on approved submittals as recommended and in strict accordance with manufacturer's written directions and as indicated on the drawings and specified herein.

- All concrete footings for athletic equipment shall be installed as indicated on the drawings and in accordance with Section 03300, Cast-in-Place Concrete.

- All sleeves required for athletic equipment installation shall be set plumb and true to line and grade in concrete as indicated on the drawings and per manufacturer's recommendation.

- All athletic equipment shall be installed in strict accordance with the latest rules, regulations and specifications governing that sport or event for which it is being installed.

3.3  		TESTING, ADJUSTMENT AND OPERATION

- All athletic equipment requiring testing, adjustments and operation shall be tested for proper operation and adjusted to conform to specified standards.

- Provide certifications as required, indicating that equipment has been tested and adjusted to conform to specified standards.

- Provide operating and maintenance instructions and manuals to Owner -designated personnel for the proper operation and care of equipment after equipment has been tested and adjusted to conform to specified standards.

3.4  		CLEANING

- Upon completion of work in any given area, remove all trash and debris from the work area and leave in clean condition.

- END OF SECTION -